## Slide 1: Parts Set Up and Initial Considerations
Hammer Bore Dimension
Hammer Center Line
Hammer angle to shank (90 ͦ std.)
Custom boring
Action elevations

## Slide 2: Calculate Hammer Bore Distances
String Height – Center Pin Height = Bore Distance
Keybed
Hammer Bore
Center Pin Height
String Height

## Slide 4: Custom Boring
As a function of unevenness of the string heights plane.

## Slide 5
Typical Steinway String Heights

## Slide 7: Hammers and Shanks
  Hammer CL and Strike-Point
    (movie)
90 degrees

## Slide 9
Shank center line
Hammer center line
Green line is 90° to shank. This line should be the hammer center line

## Slide 14: Hammer Rake Change

## Slide 15: Action Elevations
Especially the hammer shank center pin to the keybed.

## Slide 16
Make sure that the ruler contacts the workbench, and not a cross rail of the action frame!

## Slide 17
Baldwin 9’ grand. Center pin is 148 mm from keybed (workbench).

## Slide 18
Center pin height is 5.75” or 146mm, typical of many pianos such as Steinway

## Slide 19
Wip center pin height is 3- 5/16” or 84mm. The Steinway spec is 3- ¼” or 82.5mm

## Slide 20: Action and String Plane Elevations
Steinway and many others:
Keybed to hammer flange center 5.75” (146mm)
Keybed to wip flange center 3.25” (82.6mm)
Keybed to capo bar at note 62 is 7.5” (190.5mm)
  Mdl. D is 7.625” (194mm)
  Mdl. D action elevations proportionally higher as shown earlier on the Baldwin D action.

## Slide 21: END