## Slide 1: Action Geometry Theory & Practice Rick Baldassin and Nick Gravagne
40 min to 1 hour
Tucson 2019

## Slide 2: Why we analyze actions
The primary goal in evaluating a piano action is to discover the relationship of the action’s leverages to a range of complimenting hammer weights and key leads.
Secondarily, professional piano technicians should be grounded in the basics of action geometry, its nomenclature and typical ranges of ratio number.

## Slide 3: Why we analyze actions
The primary goal in evaluating a piano action is to discover the relationship of the action’s leverages to a range of complimenting hammer weights and key leads.
Secondarily, professional piano technicians should be grounded in the basics of action geometry, its nomenclature and typical ranges of ratio number.

## Slide 4
Two main considerations when reworking a grand action
Regulation
Action must regulate to 10 mm dip (+/-)
With reasonable blow of 46 mm (+/-)
With reasonable letoff of 2 mm max
With 1.25 mm aftertouch (+/-)

## Slide 5
2. Mass Re hammers and key leads
Controlling key leading and hammer weights (acceptable inertia follows).
DW and UW targets met and controlled to within acceptable limits (i.e., avg. 50 grams DW and 20 grams minimum UW).

## Slide 6
In broad strokes, both considerations are satisfied when the AR is 5:1, and when the existing (i.e. factory) hammers or replacement hammers are of suitable weight (i.e. not too heavy).
This brief overview sums up not only this class, but also the focal point of our practical action rebuilding work.
The 5:1 Action Ratio to the Rescue!

## Slide 7
Basic Blocks of Analysis and Decisions
Measure for the Standard Action Ratio (AR)
Measure for the Mass Action Ratio (AR)
Calculate for Max_Allowable Strikeweight (SW)
Adjust AR to ~5:1 ratio per Spreadsheet

## Slide 8
Strikeweight (SW) maximum calculations

## Slide 10
SWmaxA49 = (26.1 + 30) / 5.65 = 56.1 / 5.65 SWmax = 9.9 Hammer = 9.9 – 1.5 = 8.4 grams
SWmax = (26.1 + 30) / 5 = 56.1 / 5 SWmax = 11.2 Hammer = 9.9 – 1.5 = 9.7 grams

## Slide 11
Strikeweight (SW) maximums compared to typical new hammers

## Slide 12: Leverages and ratios
So what is a ratio?
And what is a leverage?

## Slide 13: What is a ratio?
What is the ratio of orange juice to apple juice?
2 c
1 c
1 cup of orange juice to 2 cups of apple juice is a 1 to 2 ratio.
OJ
AJ

## Slide 14: What is a ratio?
What is the ratio of the long stick to the short one?
24” to 8” or 24/8 or reduced is 3:1 meaning the long stick is 3 times longer than the short one.
24 inches
8 inches

## Slide 15: Ratio point of view (PoV)
When asked for a ratio of one thing to another thing, the first thing mentioned will be the first number you write down, or the numerator (top number) of a fraction.
of to

## Slide 16: Ratio point of view (PoV)
When asked for a ratio of one thing to another thing, the first thing mentioned will be the first number you write down, or the numerator (top number) of a fraction.
For example, what is the ratio of the back segment of a piano key (120 mm) to the front segment of the key (240 mm)?
Answer 120 to 240, or 120:240, or 120/240 which reduces to 1 to 2, or 1:2, or 1/2 or simply 0.50

## Slide 17: Ratio point of view (PoV) for piano actions
The correct question to ask, then, is: what is the ratio of the hammer rise (blow) to the key travel (dip) if the hammer rises 45 mm and the key travel is 9 mm?
Answer: 45 / 9 = 5

## Slide 18: The Golden Action Ratio
is 5 to 1
Meaning that for every 5 mm the hammer travels up, the key travels down1 mm

## Slide 19: The Golden Action Ratio
Real world and useful parameters are 4.8 to 5.2
with 5 being a nominal benchmark

## Slide 20: The Distance Action Ratio (DAR)
DAR = Radial Out Arms ÷ Radial In Arms

## Slide 21
Key In
Key Out
Whip In
Whip Out
Shank In
Distance Action Ration DAR Radial Arms Layouts
Shank Out

## Slide 22
Key In 260 mm
Key Out 143
Whip In 66
Whip Out 92
Shank In 21.4
Shank Out 138
Schematic View DAR Radial Arms Layouts
Go to ActGeoCompMeasure PP

## Slide 23: The Simple DAR Math
Key_O / Key_I 143 / 260 = 0.55
Whip_O / Whip_I 92 / 66 = 1.40
Shank_O / Shank_I 138 / 21.4 = 6.45
NEXT Multiply the component ratios to get the Composite AR:
DAR = 0.55 x 1.40 x 6.45 = 4.97
Notes: OPEN HO w/ calculator

## Slide 24
Key In
Key Out
Whip In
Whip Out
Shank In
Distance Action Ration DAR Radial Arms Layouts
Shank Out
What is the significance of the Radial Arms? Why do we measure on the diagonal?

## Slide 25: How and why we layout and measure the action parts
It’s all about the circles, man!

## Slide 26: How and why we lay and measure the action parts
A
B
C
D
E
F

## Slide 27: Whip Circles
Drawing by Robert Springer, RPT

## Slide 28: Whip Circles
Drawing by Robert Springer, RPT

## Slide 29: Whip Circles
Drawing by Robert Springer, RPT

## Slide 30: Whip Circles
Drawing by Robert Springer, RPT
Slowest Runner covers least distance.
Fastest Runner covers more distance.

## Slide 31
Schematic View of the DAR Radial Arms

## Slide 32
Key In
Key Out
Whip In
Whip Out
Shank In
Shank Out
Schematic View DAR Radial Arms Layouts
Go to ActGeoCompMeasure PP

## Slide 33: The Basic Action Ratio (AR)
AR = (Blow - Let-off) ÷ (Dip - Aftertouch)

## Slide 34: So, what is an Action Ratio?
It is the ratio of the hammer rise
to that of the key dip.
What is a typically good and workable Action Ratio?
~4.8 to 5.2 or average ~5

## Slide 35
Slide courtesy Baldassin - Teel

## Slide 37: ACTION RATIO COMPONENTS
Key Dip Min Nom Max 9.8 10.0 10.5 | Aftertouch Min Nom Max 1.0 1.25 1.5
Blow Distance Min Nom Max 45 46.5 48 | Let-off Min Nom Max 1.0 1.5 2.0
Slide courtesy Baldassin - Teel

## Slide 38: ACTION RATIO
(Blow Distance - Let-off) ÷ (Key Dip - Aftertouch)
(46 – 2) / (10 – 1.25)
44 / 8.75 = 5
These specifications dictate the action ratio.
Achieving this action ratio is our Primary Objective when selecting action parts for rebuilding.

## Slide 39: JOB DESCRIPTION for Distance Action Ratio (DAR)
Move Hammer a large Specified Distance (Output) by applying a small Specified Distance (Input)
8.75 mm
44 mm
Output
Input

## Slide 40: SIMPLE MACHINES
The relationship between the Output and the Input is called the Distance Ratio. In the piano, this is known as the Action Ratio.
Output
Input
AR = (Output ÷ Input)

## Slide 41: ACTION RATIO
Output = Blow Distance - Let-off
Input = Key Dip - Aftertouch
Output
Input
AR = (Output ÷ Input)
BD – LO = 46 – 2 = 44 KD – AT = 10 – 1.25 = 8.75 AR = 44 / 8.75 = 5.02
Blow Distance = 46 mm Let Off = 2 Key Dip = 10 Aftertouch = 1.25

## Slide 42: JOB DESCRIPTION for Action Ratio (AR)
Move Hammer a large Specified Distance (Output) by applying a small Specified Distance (Input)
Slide courtesy Baldassin - Teel
8.75 mm
44 mm
Output
Input

## Slide 43: SIMPLE MATH
The relationship between the Output and the Input is called the Distance Ratio. In the piano, this is known as the Action Ratio. Slide courtesy Baldassin - Teel
Output
Input
AR = (Output ÷ Input)

## Slide 44: ACTION RATIO
Output = Blow Distance - Let-off
Input = Key Dip – Aftertouch Slide courtesy Baldassin - Teel
Output
Input
AR = (Output ÷ Input)
B – L = 46 – 2 = 44 D – A = 10 – 1.25 = 8.75 AR = 44 / 8.75 = 5.02
Blow Distance = 46 mm Let Off = 2 Key Dip = 10 Aftertouch = 1.25

## Slide 45: ACTION RATIO COMPONENTS
Key Dip Min Nom Max 9.8 10.0 10.5 | Aftertouch Min Nom Max 1.0 1.25 1.5
Blow Distance Min Nom Max 45 46.5 48 | Let-off Min Nom Max 1.0 1.5 2.0

## Slide 46: ACTION RATIO
(Blow Distance - Let-off) ÷ (Key Dip - Aftertouch)
These specifications dictate the action ratio.
Achieving this action ratio is our Primary Objective when selecting action parts for rebuilding.

## Slide 47
CALCULATE ACTION RATIO
(Blow Distance - Let-off) ÷ (Key Dip - Aftertouch)
(46 mm - 2 mm) ÷ (10 mm - 1.25 mm) = 5
The AR = 5

## Slide 48
ACTION RATIOS
Minimum Nominal Maximum 4.8 5.0 5.2

## Slide 49: The AR = DAR
AR = (Blow - Let-off) ÷ (Dip - Aftertouch) = 5
DAR = Radial Out Arms ÷Radial In Arms = 5

## Slide 50: END ACTION RATIOS

## Slide 51: The Mass Action Ratio
Relates to Hammer weights and key leads.

## Slide 52: OK – let’s talk about leverages and mechanical advantage.

## Slide 53: What is a lever?

## Slide 54: Mechanical Advantage (MA) Positive
Small 10 lb. Effort here.
Lifts large 60 lb. Load here.
How could we view this setup as a negative MA?
What can we perceive about the distances moved at the effort end, and at the load end?
Wip demo and key demo

## Slide 55: JOB DESCRIPTION
Move a Mass (Output) by applying a Force (Input)
Output
Input
50 grams
9

## Slide 56
Depicting the action as one long lever
Action Ratio is 5:1
8.75 mm
44 mm
44 / 8.75 = 5
240 mm
1200 mm
1200 / 240 = 5

## Slide 57
Distance Ratio of the output to the input is 120 / 120 = 1
10 mm
10 mm
FRONT (IN)
REAR (OUT)
120 mm
120 mm
50
50
Mass ratio of the output to the input is 50 / 50 = 1

## Slide 58
10 mm
5 mm
160 mm
80 mm
50
100
Mass ratio of the output to the input is 100 / 50 = 2
Distance Ratio of the output to the input is 80 / 160 = 0.50

## Slide 59
10 mm
~3 mm
180 mm
60 mm
50
150
Mass ratio of the output to the input is 150 / 50 = 3
Distance Ratio of the output to the input is 60 / 180 = 0.33

## Slide 60
hammer
Action Ratio = Internal leverages (inc. friction)
The Hammer and Key Leads (key in balance)
10 g
DW= 50g

## Slide 61
10 g
50
Action Ratio = 5:1
Because ratio of hammer rise to dip = 44 / 8.75= 5
8.75 mm
44 mm
Depicting the action as one long lever
Mass Ratio = 1:5
Because ratio of hammer weight to DW = 10 / 50 = 0.20

## Slide 62
8.3 g
50
Action Ratio = 6:1
Because ratio of hammer rise to dip = 53 / 8.75= 6
8.75 mm
53 mm
Depicting the action as one long lever
Mass Ratio = 1:6
Because ratio of hammer weight to DW = 8.3 / 50 = 0.17

## Slide 63
7 g
50
Action Ratio = 7:1
Because ratio of hammer rise to dip = 61 / 8.75= 7
8.75 mm
61 mm
Depicting the action as one long lever
Mass Ratio = 1:7
Because ratio of hammer weight to DW = 7 / 50 = 0.14

## Slide 64: Summary
AR MR Dip Ham Rise Ham Weight
5:1 1:5 8.75 44 10.0
6:1 1:6 “ 53 8.3
7:1 1:7 “ 61 7.0
Notice that the high AR of 7 cannot support the 10 g hammer but can support the lighter 7 g hammer. The lower AR of 5 can support the 10 g hammer.

## Slide 65: Bottom Line
As the Action Ratio increased from 5:1 to 7:1 the hammer travel increased from 44 mm to 61 mm
Conclusion:
higher action ratios = more hammer travel for a given dip
lower action ratios = less hammer travel for a given dip

## Slide 66: Bottom Line
As Mass Ratio decreased from 1:5 to 1:7 the balancing hammer decreased from 10 g to 7 g
Conclusion:
lower mass ratios (e.g. 5) can handle heavier hammers
higher mass ratios (e.g. 5.7) require lighter hammers

## Slide 67
Right Angle Here
Red Arrows are Lines of Action (aka Lines of Force Vectors)
Measurements for the MAR

## Slide 68
KI
KO
WI
WO
SI
SO

## Slide 69: Schematic view
KI
KO
WI
WO
SI
SO

## Slide 70
Schematic View of the Mass Action Ratio MAR Lever Arms

## Slide 71
WO = 93 mm
SO = 130
KI = 240 mm
Measure two lengths on each action component.
KO = 120 mm
WI = 62 mm
SI = 17 mm

## Slide 72: The Simple MAR Math
Key_O / Key_I 120 / 240 = 0.50
Whip_O / Whip_I 93 / 62 = 1.50
Shank_O / Shank_I 130 / 17 = 7.65
NEXT Multiply the component ratios to get the Composite MAR:
MAR = 0.50 x 1.50 x 7.65 = 5.74
Notes: OPEN HO w/ calculator

## Slide 73
100 grams
68 grams force on the top of the jack
9
50 grams
In Physics force can be expressed as a mass and vice-versa.

## Slide 74
DAR and MAR superimposed schematic view

## Slide 75
Dr. Pfeiffer’s Lines of Action and Moment Arms (aka Lever Arms)
Forces develop through the system at right angles

## Slide 76: Determine Existing Action Ratio
AKA letting the physical action tell you what the Action Ratio is!

## Slide 77
But especially note C40 or E44
Determine Existing Action Ratio
Measure string height of several notes

## Slide 78: Determine Existing Action Ratio
Set String Height Gage
Hi-Gage Square Attachment from Garrett Wade

## Slide 79: Determine Existing Action Ratio
Set Let-off (2 mm)
Action is now out of the piano, sitting on a dolly / bench. Let off is being set to 2 mm or 1.5 mm

## Slide 80: Finding a Practical Action Ratio
Set letoff to 2 mm (or 1.5 mm).
Set dip to 10 mm (or other valid value).
Insert 1.25 mm aftertouch gage.
Turn capstan up or down until hammer just lets off with firm (but not crushing) pressure at the front key end.
The resulting blow is what works for this set of dip, aftertouch and letoff numbers.

## Slide 81
Letoff = 2mm
Step 1 -- set letoff

## Slide 82
10 mm dip block
Step 2 -- set dip

## Slide 83
1.25 mm aftertouch gage
Step 3 -- insert AT gage

## Slide 84
45 mm blow
Step 4 -- adjust capstan up or down until hammer just lets off (firm pressure on key with finger).
The resulting blow dimension (here 45 mm) is now a function of letoff, dip and aftertouch, and is the dimension we use in the following simple formula.

## Slide 85: Here the Action Ratio is good AR = (Blow – Let off) / (Dip – Aftertouch) = (45 – 2) / (10 – 1.25) = 43 / 8.75 AR = 4.91 i.e. ~ 5 ish
Range of Action Ratios: 4.80 to 5.20

## Slide 86: Big Red Flag for Possible Action Trouble
15.5 mm
May not be able to support modern heavier hammers
Short 15.5 mm knuckle distance = higher action ratio

## Slide 87: Big Red Flag for Possible Action Trouble
240 mm
130 mm
Key ratio too long @ 130 / 240 = 0.54 or 1.85 to 1
So Higher Action ratio here!

## Slide 88: Big Red Flag for Probable Action Trouble
The double-whammy of the long key ratio and the short knuckle dimension typically means that the action will not support modern hammers.
Changing the knuckle distance to 16.2 mm or 17 mm (sometimes a capstan relocation may be required) will solve the problem.
So, the very first thing to check is the key ratio and the knuckle location.

## Slide 89: Big GREEN Flag for Probable Action GOOD
240 mm
120 mm
Key ratio good @ 120 / 240 = 0.50 or 2 to 1
17 mm

## Slide 90: Hammer Bore Basics

## Slide 91
But especially note C40 or E44
Measure string height of several notes

## Slide 92: Hammer Bore Basics
148 mm from keybed to flange center

## Slide 93: Hammer Bore Basics
Hammer Bore Example:
190 mm = String height off keybed
- 146 mm = Hammer flange height off flat workbench
44 mm = Hammer bore
44 mm

## Slide 94
Action and String Plane Elevations
Steinway spec for action elevations:
Keybed to hammer flange center is 5.75” (146 mm)
Keybed to whippen flange center is 3.25” (82.55 mm)
Keybed to underside of capo bar at note 62 is 7.5” (190.5 mm)
  7.625” (194 mm) on the Model D
  Model D action elevations are usually higher as well as shown below regarding the Baldwin Concert grand action.

## Slide 95: Using the Action Geometry Program
Take measurements
Input measurements into program
Run the program
Interpret readouts
If necessary, adjust knuckle and / or capstan location to attain target AR (e.g. 5:1)

## Slide 96: Downloads
Action Program gravagne.com/AGP_Tucson.xlsm
gravagne.com/AGPTucsonLITE.xlsx
PowerPoint gravagne.com/TucsonPP.pptx
Key weigh off
gravagne.com/KBM.doc

## Slide 97: Using the Action Geometry Program
Take measurements
  Key – two measurements
  Wippen – two measurements
  Shank – two measurements
  Action Spread – one measurement